## Slide 1: Semantics-aware Intrusion Detection for Industrial Control Systems
Ömer Yüksel
Jerry den Hartog
Sandro Etalle
Notes: TU/e Security group

## Slide 2: About Me
Ömer Yüksel
PhD candidate in Eindhoven University of Technology, Security group (2014- )
Research interests: intrusion detection, data analytics

## Slide 3: SpySpot Project
http://security1.win.tue.nl/spyspot/
Scientific Partners
Industrial Partners
Notes: Dutch national, Vis&Sec

## Slide 4: Targeted attacks
Attacker
Initial compromise
Sabotage
Exfiltration
Privilege
escalation
Propagation

## Slide 5: Industrial Control Systems (ICS)
Notes: ICS used in energy distribution, power plants, manufactoring etc.
Building blocks, explain layers, HMI, PLC, Historian

## Slide 6: Industrial Control Systems (ICS)

## Slide 7: Threat Model
Assets to protect:
Network hosts: PLC, HMI, Control Server, …
Field devices: Heater, sensors, pipeline, …

## Slide 8: Threat Model
System-related attacks
  e.g. Buffer overflow
Process-related attacks
  e.g. “Change the rotation speed”
Reconnaissance
  e.g. Map out all valid register addresses
Notes: Stuxnet -> threat categories

## Slide 9: Protection of ICS Networks
Attack patterns are unpredictable.
  Cannot rely on signature-based systems
Availability must not be impaired.
  Cannot use preventative systems (e.g. access control)
Attacks can be carried out by sending a single malicious message.
  Cannot rely on flow-based detection
Networks traffic contains large and diverse communication patterns.
  Manual whitelisting is infeasible
Notes: 1-Need anomaly detection 2-Need IDS 3-Need to look at the content (payload) 4-Need it to be automated

## Slide 10: Protection of ICS Networks
Attack patterns are unpredictable.
  Cannot rely on signature-based systems → Anomaly detection
Availability must not be impaired.
  Cannot use preventative systems (e.g. access control) → IDS
Attacks can be carried out by sending a single malicious message.
  Cannot rely on flow-based detection → Payload-based
Networks traffic contains large and diverse communication patterns.
  Manual whitelisting is infeasible → Data-driven
Notes: 1-Need anomaly detection 2-Need IDS 3-Need to look at the content (payload) 4-Need it to be automated

## Slide 11: Anomaly-based Approaches
Payload information
Network&transport header
Byte string
Protocol syntax
Protocol semantics
IP Header
TCP Header
Payload
Src :10.10.10.11 Src:502 0a030203e8...
Dst: 10.10.10.20 Dst: 50269
Src :10.10.10.11 Src:502 0a030203e8...
Dst: 10.10.10.20 Dst: 50269
Src :10.10.10.11 Src:502 0x0a 0x03 0x02 0x03e8
Dst: 10.10.10.20 Dst: 50269
Unit id
Function
Our approach
Return value
Src :10.10.10.11 Src:502 0x0a 0x03 0x02 1000 Dst: 10.10.10.20 Dst: 50269
Src :10.10.10.11 Src:502 10 read (3) 2 1000
Dst: 10.10.10.20 Dst: 50269
Par. Length
Return value
(numeric)
Return value
(numeric)
Par. Length
(numeric)
Function
(nominal)
Unit id
(nominal)
Previous work
Notes: Issues: single message attacks, false alerts, black box, limited setting, extensive domain knowledge

## Slide 12: Current Issues
  Unable to detect certain single-message attacks,
  Too many false alerts to work in practice,
  Model or alerts are not user-understandable,
  Limited to a specific protocol or setting,
  Requires extensive domain knowledge.
Payload information
Network&transport header
Byte string
Protocol syntax
Protocol semantics

## Slide 13: Semantics-aware Intrusion Detection
We propose a payload-based network intrusion detection framework that is:
Semantics-aware
  Considers the protocol fields and value types in the payload.
Anomaly-based
  Uses network traffic data to build a model of the “normal traffic”.
General purpose
  Can be instantiated on any protocol where a parser is available (we test on S7 and Modbus)
White-box [1]
  User-understandable model based on simple probabilities.
  Can be updated or corrected by an operator.
  Displays meaningful alerts.
Src :10.10.10.11 Src:502 10 read (3) 2 1000
Dst: 10.10.10.20 Dst: 50269
Return value
(numeric)
Par. Length
(numeric)
Function
(nominal)
Unit id
(nominal)
[1] Costante, E., Hartog, J. den, Petković, M., Etalle, S., & Pechenizkiy, M. (2014). Hunting the Unknown.

## Slide 14: General Framework
Message: The PDU of an ICS-specific protocol.
The messages are interpreted by external component, e.g. Wireshark protocol dissector.
We focus on single-message attacks in this work.

## Slide 15: Feature Extraction
We use protocol fields to extract features from the traffic.
Feature categories:
  Elementary:
    Numeric: e.g. parameter length
    Nominal: e.g. function, protocol identifier
  Compound: e.g. <function, parameter length>

## Slide 16: Feature Selection
Feature selection is performed by the expert setting up the model.
Non-helpful features are discarded, such as those that are:
  seemingly random (e.g. nonces)
  sequential (e.g. counters)
  have an erratic behavior (displaying a high variance/entropy etc.)


## Slide 17: Detection Model
Our model of normal traffic consists of probability distributions per feature.
We build the model using samples from normal traffic.
Rare values are considered anomalous.
Chart: 
| read_register | write_register | diagnostics
 | 0.6 | 0.3 | 0.1
Function
Chart: 
| 0x1000 | 0x2000 | 0x4000
 | 0.5 | 0.4 | 0.1
Register address

## Slide 18: Profiling
Normal traffic contains a mixture of different behavior patterns.
Profiling allows detecting contextual anomalies.
Chart: 
| read_register | write_register | diagnostics
 | 0 | 0.73 | 0.27
Chart: 
| read_register | write_register | diagnostics
 | 0.95 | 0.05 | 0
Chart: 
| read_register | write_register | diagnostics
 | 0.6 | 0.3 | 0.1
PLC-1
HMI-1

## Slide 19: Binning
Numeric features tend to yield a large number of unique values.
Therefore we consider the distribution of ranges instead.
Chart: 
| <5 | 6-10 | 11-15
0.5 0.3 0.2 | 0.5 | 0.3 | 0.2
data length

## Slide 20: Alerts
If a feature yields a rare value (or bin), an alert is raised.
We use a threshold to determine the model’s strictness.
  i.e. raise an alert if a value has a less than 10% probability of occurrence.
The framework displays the features causing the alert.
Chart: 
| read_register | write_register | diagnostics
 | 0.95 | 0.05 | 0
Src :10.10.10.11 Src:502 10 diagnostics(8)
Dst: 10.10.10.20 Dst: 50269
Function
(nominal)
Unit id
(nominal)
IP Header
TCP Header

## Slide 21: Evaluation
False Positive Rate
Detection Rate

## Slide 22: Evaluation
Datasets:
  Modbus-RTU: Serial communication
    Lab setting (Mississippi State University)
    Preprocessed by the providers, raw traffic not available
  S7 Communication: Siemens devices
    Operational ICS
    Raw network traffic, parsed with Wireshark
Attacks:
  Modbus-RTU: Reconnaissance and process-related
  S7: Reconnaissance and system-related attacks
    Publicly available at (http://descrics.com/)

## Slide 23: Compared Approaches
McPad [1]
  N-gram analysis
Attributed token kernel [2]
  N-gram analysis
  Utilizes protocol syntax
Both methods utilize one-class support vector machines (SVM) to model normal traffic.
  [1] Perdisci, R., Ariu, D., Fogla, P., Giacinto, G., & Lee, W. (n.d.). McPAD : A Multiple Classifier System for Accurate Payload-based Anomaly Detection, (October 2008).
  [2] Düssel, P., Gehl, C., Laskov, P., & Rieck, K. (2008). Incorporation of application layer protocol syntax into anomaly detection. Information Systems Security, 188–202.
Notes: Text-based protocols

## Slide 24: Results (I)
Experiments with elementary features only:
Approach | Detection Rate | False Positive Rate
McPad | 100% | 20.2%
Attributed token kernel | 99.9% | 33%
White-box framework | 100% | 0.04%
Approach | Detection Rate | False Positive Rate
Attributed token kernel | 91% | 27%
White-box framework | 97.3% | 0.08%
Modbus-RTU
S7

## Slide 25: Results (II)
For Modbus-RTU dataset, we create compound features using semantically related elementary features, e.g. <SetPoint, DeltaSetPoint>
Approach | Detection Rate | False Positive Rate
White-box framework (elementary features only) | 97.3% | 0.08%
 | 100% | 16.7%
White-box framework (w/ compound features) | 100% | 0.57%

## Slide 26: Alert causes
Features causing majority of the alerts in the detected attacks:
Modbus-RTU
  Time Interval
  Pipeline pressure
  Set point
S7
  Data length
  ROSCTR (Remote operating service control)
  Parameter count
  Function

## Slide 27: Performance
Time complexity:
  Training: Linear to the dataset size
  Detection: constant time
Can be scaled to larger networks by utilizing profiling.
Parsing is the main bottleneck in the current implementation.
  Processing a single message: 0.97msec
  Parser overhead: 0.7msec

## Slide 28: Conclusions
N-gram analysis is not practical on binary protocols.
Utilizing the right features is more important than creating a complex model of normal behavior.
Using a simple model allows a human operator to correct and update the model, and results in alerts containing actionable information.

## Slide 29: Visualization
Integration with a visual interface for displaying alerts and traffic in detail and updating the model.
Bram Cappers <b.c.m.cappers@tue.nl>
https://www.youtube.com/watch?v=aYywTOYjYDA

## Slide 30: Future Work
Feature selection
  Metrics of “feature quality“
  Designer interface
Feature construction
Application to other domains
  Back office traffic
Detection of sequential attacks
  Looking at sessions or groups of messages

## Slide 31: Thank you
o.yuksel@tue.nl
Project: http://security1.win.tue.nl/spyspot/
Notes: Datasets?

## Slide 32: Tuning
Human operator can update the model by modifying bins or thresholds.