## Slide 1: EV CAN-bus Man-in-the-Middleing
for fun and profit
Emile Nijssen

## Slide 7: You’re probably an engineer

## Slide 15: Problems with old electric cars
Limited range
Slow charging
No cool new gadgets

## Slide 16: Not solutions
Add extra batteries
Increase charging speed
Add cool gadgets
Solutions
Buying a different car

## Slide 17: Solutions in practice?

## Slide 19: So you say it’s possible?

## Slide 20: Commercial incentives push projects to completion

## Slide 21: Why?

## Slide 24: CAN-bus 101
Two-wire differential bus
All devices share the bus
Extremely rugged
  Differential signalling over twisted pair
  Built-in CRC
  Bit-stuffing
  Automatic retransmit
  Bus-off/passive modes for startup
  Fairly slow, up to ~1Mbit/s

## Slide 25: But CAN is also very simple
ID
(11 or 29 bits)
Data
(1-8 bytes)

## Slide 26: Consequences of CAN
Bus is shared
  > no directionality (everybody can be bus master)
  > nodes have to wait for others to stop talking
  > no definite timing or ordering
Messages are short
  > you have to be thrifty with your messages
  > no real opportunity for encryption or handshaking

## Slide 28
Electron/brake pedal?

## Slide 29
Electron/brake pedal

## Slide 31
MITM here

## Slide 33
First column shows direction of messages

## Slide 34
Second column shows ID

## Slide 35
Third column shows data

## Slide 36
So, we’re interested in motor control messages
Gotta be pretty frequent
Have to go from VCM to inverter
Plausible motor control data?

## Slide 37
The 1>2 direction comes from the VCM
(this is how I wired it up)
So forget about all 2>1 messages

## Slide 38
Hey, there are only three Ids
Two of which happen frequently: 1D4 and 1F2

## Slide 39: Do a trace while driving
1F2 doesn’t do squat while driving. So motor control message has to be 1D4

## Slide 40: 1D4 trace
Byte 0,1,4[3:0],5,6 are static

## Slide 41: 1D4 trace
Last byte varies WILDLY

## Slide 42: 1D4 trace
CRC!
Why? CAN has a CRC built in. This is a waste of a valuable byte!

## Slide 43: 1D4 trace
Around Byte 4 is periodic

## Slide 44: 1D4 trace
This HAS to be the motor control word

## Slide 46: Increase reported battery capacity
By modifying CAN message 5bc byte 0-1[7:6]

## Slide 47: Increase regenerative braking

## Slide 48: Give an 8 year old leaf the range of a Tesla Model 3

## Slide 49: If there’s still time: TCU

## Slide 50: MITM is not just a security issue