## Slide 1: Starbleed A Full Break of the Bitstream Encryption of Xilinx 7-Series FPGAs
Maik Ender, Amir Moradi, Christof Paar
Hardwear.io

## Slide 2
https://www.reddit.com/r/ElectricalEngineering/comments/g6vaey/ u/iguetesilva

## Slide 3: Starbleed A Full Break of the Bitstream Encryption of Xilinx 7-Series FPGAs
Maik Ender, Amir Moradi, Christof Paar
Hardwear.io

## Slide 4
Field Programmable Gate Arrays
Field Programmable Gate Array (FPGA)
Special IC
Reprogrammable logic
Bitstream
program
Photo by Patrick Tomasso on Unsplash
Photo by Chuanchai Pundej on Unsplash
Photo by American Public Power Association on Unsplash
Photo by Mario Caruso on Unsplash
Bitstream contains FPGA‘s design
Stored on external memory
FFFFFFFF
AA995566
"StartDec"
"WrCntr0"
02003FE5
Notes: Determine their functionality after manufacturing
Telecommunications
Industrial control systems
Aerospace
Military
Artificial Intelligence
Datacenters
Bitstream = firmware (simplification)

## Slide 5
Bitstream Security
Bitstream
FFFFFFFF
AA995566
"StartDec"
"WrCntr0"
02003FE5
program
Photo by Patrick Tomasso on Unsplash
Photo by Chuanchai Pundej on Unsplash
Photo by American Public Power Association on Unsplash
Photo by Mario Caruso on Unsplash
Bitstream security is vital
  Design cloning
  Reverse engineering
  Design manipulation
  Hardware Trojans
Notes: Assured
interdict
Algorithms
Intellectual property
implant

## Slide 6
Bitstream Encryption
Bitstream
FFFFFFFF
AA995566
"StartEnc"
"WrCntr0"
02003FE5
Bitstream encryption
Confidentiality: bitstream is encrypted
Authenticity: FPGA loads only designs from integrator
Integrity: Bitstream is not changed
Key Fuses/BBRAM
CRYPTO
FPGA
encrypted program
AES-256
HMAC
Notes: Hides the bitstream conted from the adversary

## Slide 7
Attack
Bitstream
FFFFFFFF
AA995566
"StartEnc"
"WrCntr0"
02003FE5
Bitstream encryption
Confidentiality: bitstream is encrypted
Authenticity: FPGA loads only designs from integrator
Integrity: Bitstream is not changed
Starbleed Attack I: Break Confidentiality
Starbleed Attack II: Break Authenticity
okay
Key Fuses/BBRAM
CRYPTO
FPGA
encrypted program
please decrypt the bitstream
Manipulate the encrypted bitstream
Notes: Hides the bitstream conted from the adversary

## Slide 8
HOW TO PROGRAM AN FPGA?

## Slide 9
Configuration Engine
FDRO
…
Status
Control 0
WBSTAR
FDRI
Fabric
Configuration Engine
Configuration Registers
Bitstream
Dec?
DEC
JTAG
"Header"
"StartDec"
HMACHead
"WrCntr0"
02003FE5
"WrFDRI"
COFFEEEE
BADB0070
HMAC tag
Encrypted
FPGA
Notes: Abstract model
Frame data register in
Writes to this register configure frame data at the frame address specified in the FAR register.
Frame data register out
20 documented registers

## Slide 10
Bitstream Program
FDRO
…
Status
Control 0
WBSTAR
FDRI
Fabric
Configuration Engine
Configuration Registers
Bitstream
Dec?
DEC
JTAG
"Header"
"StartDec"
HMACHead
"WrCntr0"
02003FE5
"WrFDRI"
COFFEE
BADB0070
HMAC tag
"Header"
"StartDec"
HMACHead
"WrCntr0"
02003FE5
"WrFDRI"
COFFEEEE
BADB0070
HMAC tag
FPGA
Notes: authenticity

## Slide 11
Read Register
FDRO
…
Status
Control 0
WBSTAR
FDRI
Fabric
Configuration Engine
Configuration Registers
Bitstream
Dec?
DEC
JTAG
FFFFFFFF
AA995566
"Rd STAT"
"WrCntr0"
02003FE5
"WrFDRI"
COFFEE
FFFFFFFF
AA995566
"Rd STAT"
I am fine
FPGA
BADB0070
C00FFEE

## Slide 12
ATTACK I BREAKING CONFIDENTIALITY

## Slide 13
FPGA
Attack
FDRO
…
Status
Control 0
WBSTAR
FDRI
Fabric
Configuration Engine
Configuration Registers
Bitstream
Dec?
DEC
JTAG
"Header"
"StartDec"
HMACHead
"WrCntr0"
02003FE5
WrWBSTAR
COFFEEEE
BADB0070
HMAC tag
"Header"
"StartEnc"
HMACHead
"WrCntr0"
02003FE5
"WrFDRI"
COFFEEEE
BADB0070
"Header"
"StartDec"
HMACHead
"WrCntr0"
02003FE5
"WrWBSTAR"
COFFEEEE
BADB0070
The FPGA notices the manipulation (HMAC invalid) and resets
HMAC tag
Exploit CBC malleability
COFFEEEE
divert
Cut bitstream

## Slide 14
MultiBoot – Documentation
Notes: Readout
The FPGA MuliBoot feature enables switching between images on the fly
Warm boot start address (WBSTAR) register

## Slide 15
Attack – Readout
FDRO
…
Status
Control 0
WBSTAR
FDRI
Fabric
Configuration Engine
Configuration Registers
Dec?
DEC
JTAG
COFFEEEE
Bitstream
"Header"
RdWBSTAR
"Header"
RdWBSTAR
FPGA
The FPGA notices the manipulation (HMAC invalid) and resets
HMAC tag
02003FE5
COFFEEEE
divert

## Slide 16
Configuration Registers
The FPGA notices the manipulation (HMAC invalid) and resets
FPGA
Attack – Overview
FDRO
…
Status
Control 0
WBSTAR
FDRI
Fabric
Configuration Engine
Dec?
DEC
JTAG
COFFEEEE
WrWBSTAR
"Header"
"StartDec"
HMACHead
"WrCntr0"
02003FE5
"WrWBSTAR"
COFFEEEE
BADB0070
"Header"
RdWBSTAR
2) Readout Bitstream
1) Manipulate the bitstream
4) Read out the WBSTAR register
3) Resets the FPGA (automatically)
2) Configure the FPGA with the malicious bitstream
5) Reset the FPGA (manually)
HMAC tag
1) Manipulated Bitstream
Leak one bitstream word (32 bits)
Notes: 7.9 miliseconds
7K160T -> 3:42
7VX1140T -> roughly a day

## Slide 17
Bitstream security is vital
Design cloning
Reverse engineering
Design manipulation
Hardware Trojans
Bitstream Security
Photo by Patrick Tomasso on Unsplash
Photo by Chuanchai Pundej on Unsplash
Photo by American Public Power Association on Unsplash
Photo by Mario Caruso on Unsplash
?
?
Attack I: Break Confidentiality
= Attacker can decrypt bitstream
?
Notes: Assured
interdict

## Slide 18
ATTACK II BREAKING AUTHENTICITY

## Slide 19
Attack I: Decrypt the bitstream
HMAC (still) assures authenticity
Any manipulation is detected
HMAC key can be decrypted by attack I
Forge new valid HMAC tags
Encrypt new/manipulated bitstreams:
  Decryption oracle + CBC malleability = encryption oracle
  Know attack: ‘‘Practical padding oracle attacks‘‘ Rizzo et al. WOOT 2010
Attack II: Breaking Authenticity
Bitstream
"Header"
"StartEnc"
HMACHead
"WrCntr0"
02003FE5
"WrFDRI"
COFFEEEE
BADB0070
HMAC tag
HMAC key
CRYPTO
FPGA
okay
please decrypt the bitstream
Attacker can forge valid HMAC tags
Notes: Juliano Rizzo and Thai Duong. Practical padding oracle attacks. 4th USENIX Workshop WOOT 2010.

## Slide 20
Bitstream Security
Photo by Patrick Tomasso on Unsplash
Photo by Chuanchai Pundej on Unsplash
Photo by American Public Power Association on Unsplash
Photo by Mario Caruso on Unsplash
Attack II: Break Authenticity
?
?
Attack I: Break Confidentiality
Bitstream security is vital
Design cloning
Reverse engineering
Design manipulation
Hardware Trojans
?
FULL BREAK OF THE BITSTREAM ENCRYPTIO
Notes: Assured
interdict

## Slide 21
WHAT WENT WRONG?

## Slide 22
‘‘Use before validate‘‘ (Attack I)
HMAC key stored inside the encrypted bitstream (Attack II)
What Went Wrong?
Bitstream
"Header"
"StartDec"
HMACHead
"WrCntr0"
02003FE5
"WrFDRI"
COFFEEEE
BADB0070
HMAC tag
Commands interpreted before HMAC validation
HMAC key
Attacker can forge valid HMAC tags
Notes: As far as we break the confidentiality we break the authenticity

## Slide 23
COUNTERMEASURES
&
DEFENSE TECHNIQUES

## Slide 24
Countermeasures & Defense Techniques
 | New Devices | New Series | Current 7-Series
Validate before use | • | • | 
Patchable Encryption | • | • | 
IFA, Model Checker | • |  | 
OpenSource Hardware | • |  | 
Obfuscation |  |  | 
Revision Select PIN |  |  | 

## Slide 25
Countermeasures & Defense Techniques
 | New Devices | New Series | Current 7-Series
Validate before use | • | • | 
Patchable Encryption | • | • | 
IFA, Model Checker | • |  | 
OpenSource Hardware | • |  | 
Obfuscation |  |  | 
Revision Select PIN |  |  | 
Countermeasures
  Validate the bitstream before interprete by the configuration engine

## Slide 26
Countermeasures & Defense Techniques
 | New Devices | New Series | Current 7-Series
Validate before use | • | • | 
Patchable Encryption | • | • | 
IFA, Model Checker | • |  | 
OpenSource Hardware | • |  | 
Obfuscation |  |  | 
Revision Select PIN |  |  | 
Countermeasures
  Validate the bitstream before interprete by the configuration engine
  Patchable bitstream encryption in the reconfigurable fabric
Notes: It is a bit ironic that the bitstream encryption is not reprogrammable in a reprogrammable device

## Slide 27
Countermeasures & Defense Techniques
 | New Devices | New Series | Current 7-Series
Validate before use | • | • | 
Patchable Encryption | • | • | 
IFA, Model Checker | • |  | 
OpenSource Hardware | • |  | 
Obfuscation |  |  | 
Revision Select PIN |  |  | 
Countermeasures
  Validate the bitstream before interprete by the configuration engine
  Patchable bitstream encryption in the reconfigurable fabric
General defense techniques
  Attack already visible in documentation  specification is flawed
Notes: Not fomaly verify the HDL code since the specification is already flawed
Does not leak any confidential data

## Slide 28
Countermeasures & Defense Techniques
 | New Devices | New Series | Current 7-Series
Validate before use | • | • | 
Patchable Encryption | • | • | 
IFA, Model Checker | • |  | 
OpenSource Hardware | • |  | 
Obfuscation |  |  | 
Revision Select PIN |  |  | 
Countermeasures
  Validate the bitstream before interprete by the configuration engine
  Patchable bitstream encryption in the reconfigurable fabric
General defense techniques
  Attack already visible in documentation  specification is flawed
  OpenSource transparency
    Follow Kerckhoffs Principle "Everything except the key is known"
    OpenTitan

## Slide 29
Countermeasures
  Validate the bitstream before interprete by the configuration engine
  Patchable bitstream encryption in the reconfigurable fabric
General defense techniques
  Attack already visible in documentation  specification is flawed
  OpenSource transparency
    Follow Kerckhoffs Principle "Everything except the key is known"
    OpenTitan
Countermeasures & Defense Techniques
 | New Devices | New Series | Current 7-Series
Validate before use | • | • | 
Patchable Encryption | • | • | 
IFA, Model Checker | • |  | 
OpenSource Hardware | • |  | 
Obfuscation |  |  | 
Revision Select PIN |  |  | 

## Slide 30
Still same functionality
‘‘Harder‘‘ to reverse engineer
Raise-the-bar countermeasure only
Obfuscation
https://www.flickr.com/photos/curious_e/
Photo by American Public Power Association on Unsplash
Notes: The design is tangled
Expense
costs

## Slide 31
Revision Select PIN
Key BBRAM
CRYPTO
FPGA
PCB
WBSTAR
Power (Vcc)
RS Pins
Vcc
Reset Logic
CLEAR
Revision select pins Drive output pin on next warm boot
1
1
Modify PCB Wire RS pin to a reset logic
If RevisionSelect ≠ 0
  Reset FPGA
  Remove BBRAM key power to clear encryption key
Attacker can still modify the PCB
Value default 0
During attack leaks bitstream content ≠ 0
Notes: Placed on a PCB
We use this to our advantage
brick

## Slide 32
Conclusion
Attack II: Break Authenticity
Attack I: Break Confidentiality
manipulating the bitstream
Full break of confidentiality and authenticity
Only access to configuration interface needed
Xilinx 7-Series and (partially) Virtex-6 affected
For current devices only raise-the-bar countermeasures
General defense techniques: Verify the specification, OpenSource
decrypting the bitstream
@MaikEnderEU
https://www.usenix.org/conference/usenixsecurity20/presentation/ender
Notes: Assured
interdict
This was how we break the bitstream encryption using the bitstream encryption
Formal verification methods